## Slide 1
PERA Architecture Levels in Process Industries
MLM-007-B
Turn on your audio and click start to begin video
Industry | Process Industry
Principal Role | Owner / Operator
Professional Role | Control Engineers + IT Specialists
Enterprise Phase | All
Notes: This MLM provides an introduction to the concept of PERA Architecture Levels in process industry plants. It is intended for Control Engineers and IT Specialists who will define these systems and the associated industrial and IT networks, maintain, and/or develop them in the future.
Click the START button when you are ready to advance to the next slide.

## Slide 2
PERA defines three types of Enterprise Architecture:
Facilities Architecture
Human and Organizational Architecture
Control & Information Systems Architecture
Control and Information Systems are further divided into Logical and Physical System Architectures.
Enterprise
Inception
Enterprise
Dissolution
Facilities
People
Control
& Info
Systems
PFDs and
P&IDs
Defined by
Documents
such as:
WHAT IS AN ENTERPRISE ARCHITECTURE ?
Physical System
Architecture
Logical &
Org Charts &
Position
Descriptions
Notes: PERA defines three types of Enterprise Architecture:
Facilities Architecture
Human and Organizational Architecture
Control & Information Systems Architecture
Control and Information Systems are further divided into Logical and Physical System Architectures.

## Slide 3
The Control and Information Systems of a process plant, pipeline, oil field or other process facility has an inherent structure, called an “Architecture.
This Control and Information Architecture consists of :
  a Physical Architecture (Computer Hardware and Network Devices and Media), and
  a Logical Architecture (Enterprise Systems, Application Software, and Protocols).
The “PERA Levels” within this architecture may be characterized by a “Time Base” which may be expressed in terms of “4R’s”:
Response Time delay between reading and reaction
Resolution Time between readings
Reliability Time between failures of readings or reaction
Resilience Time to restore readings or resistance to failure or cyberattack
System Architecture Design
Notes: The Control and Information Systems of a process plant, pipeline, oil field or other process facility has an inherent structure, called an “Architecture.
This Control and Information Architecture consists of :
a Physical Architecture (Computer Hardware and Network Devices and Media), and
a Logical Architecture (Enterprise Systems, Application Software, and Protocols).
The “PERA Levels” within this architecture may be characterized by a “Time Base” which may be expressed in terms of “4R’s”:
Response Time delay between reading and reaction
Resolution Time between readings
Reliability Time between failures of readings or reaction
Resilience Time to restore readings or resistance to failure or cyberattack

## Slide 4
NETWORKS
OPER.
DISP.
OPER.
DISP.
MAINT'CE
PRODUCT
OFFICE
CORP & DIVISIONAL
SITEWIDE
LOCAL
ENG/TECH
MGT
QUALITY
MGT
TRACKING
PROCESS
SUPRV.
AREA 1
INDUSTRIAL
LAN
LAN
R
WIDE
AREA
NETWORK
CORP & DIVISIONAL
CONTROLLERS, PLC'S, DATA ACQUISITION DEVICES, ETC.
PROPRIETARY
DCS AND PLC
PROCESS
SUPRV.
AREA 3
AUTOMAT'N
WAREH'SE
PROCESS
SUPRV.
AREA
2
PROD'N
REPORT
& SCHED
POWER
SUPRV.
HOUSE
OPER.
DISP.
OPER.
DISP.
DP & MIS
ENG. &
TECH
6 & 7
5
4
3
1
2
OPER.
DISP.
SITEWIDE
DATABASE
LOCAL
DP/MIS
PROCESS PLANT PHYSICAL ARCHITECTURE
Here is a typical Physical Architecture for a Process Industry Plant.
Notes: Here is a typical Physical Architecture for a Process Industry Plant.
In this enterprise 7 Architectural Levels have been defined.

## Slide 5
NETWORKS
OPER.
DISP.
OPER.
DISP.
MAINT'CE
PRODUCT
OFFICE
CORP & DIVISIONAL
SITEWIDE
LOCAL
ENG/TECH
MGT
QUALITY
MGT
TRACKING
PROCESS
SUPRV.
AREA 1
INDUSTRIAL
LAN
LAN
R
WIDE
AREA
NETWORK
CORP & DIVISIONAL
CONTROLLERS, PLC'S, DATA ACQUISITION DEVICES, ETC.
PROPRIETARY
DCS AND PLC
PROCESS
SUPRV.
AREA 3
AUTOMAT'N
WAREH'SE
PROCESS
SUPRV.
AREA
2
PROD'N
REPORT
& SCHED
POWER
SUPRV.
HOUSE
OPER.
DISP.
OPER.
DISP.
DP & MIS
ENG. &
TECH
6 & 7
5
4
3
1
2
OPER.
DISP.
SITEWIDE
DATABASE
LOCAL
DP/MIS
IT vs. ICS in TRADITIONAL PLANT ARCHITECTURES
Traditionally, IT (data storage, analysis & presentation) predominated at higher levels in the architecture.
Control Systems were often described as “Industrial Control Systems” or ICS.
Traditional IT vs. ICS split
IT
ICS
Notes: Traditionally, IT (data storage, analysis & presentation) predominated at higher levels in the architecture to the extent that OT was often described as “Industrial Control Systems” or ICS.

## Slide 6
NETWORKS
OPER.
DISP.
OPER.
DISP.
MAINT'CE
PRODUCT
OFFICE
CORP & DIVISIONAL
SITEWIDE
LOCAL
ENG/TECH
MGT
QUALITY
MGT
TRACKING
PROCESS
SUPRV.
AREA 1
INDUSTRIAL
LAN
LAN
R
WIDE
AREA
NETWORK
CORP & DIVISIONAL
CONTROLLERS, PLC'S, DATA ACQUISITION DEVICES, ETC.
PROPRIETARY
DCS AND PLC
PROCESS
SUPRV.
AREA 3
AUTOMAT'N
WAREH'SE
PROCESS
SUPRV.
AREA
2
PROD'N
REPORT
& SCHED
POWER
SUPRV.
HOUSE
OPER.
DISP.
OPER.
DISP.
DP & MIS
ENG. &
TECH
6 & 7
5
4
3
1
2
OPER.
DISP.
SITEWIDE
DATABASE
LOCAL
DP/MIS
With Enterprise Integration, “Digital Twin” Plant Optimization, AI-based Logistics, and MRP systems, “high level” applications increasingly involve real-time data acquisition and regulatory control.
ICS
IT vs. OT in “INDUSTRY 4.0” PLANT ARCHITECTURES
IT
Industry 4.0 IT vs. OT split
New OT
Notes: With Enterprise Integration, “Digital Twin” Plant Optimization, AI-based Logistics, and MRP systems, more and more “high-level” applications involve real-time data acquisition and regulatory control.
OT is often used to describe the combination of new Operational Technology and conventional ICS systems.
Control Engineers often retain the conventional Industrial Control System (ICS) term, and use the OT definition only for applications that include IT infrastructure. This was the original Gartner definition of OT, but this is awkward, as it does not identify what professional skills are required.
PERA prefers to use the OT term for systems where Control Systems and IT professionals work together. In this case, Control Engineers are responsible for ICS, IT Specialists are responsible for IT systems, and OT systems by definition require them to work together.

## Slide 7
ENGINEERING ROLES in PLANT ARCHITECTURES
OT and IT applications exist at all levels of the Enterprise. The Risks associated with each application determine what Skills are needed to mitigate those Risks to meet company standards.
Required Engineering skills might include Control Engineers, Industrial Network Engineers, Electrical Engineers, etc.
Engineering skills may be needed where:
  - Failures have severe consequences (at any level in the Enterprise Architecture. For example,
    (OT) Control and optimization of reactors, compressors, or other hazardous equipment
    (IT) Continuous Environmental Monitoring Systems (CEMS) that may result in fines and/or plant shutdown.
  - Special equipment and network design are required for hazardous areas (e.g., Industrial networks, firewalls, etc.).
Notes: OT and IT applications exist at all levels of the Enterprise. The Risks associated with each application determine what Skills are needed to mitigate those Risks to meet company standards.
Required Engineering skills might include Control Engineers, Industrial Network Engineers, Electrical Engineers, etc.
Engineering skills may be needed where:
Failures have severe consequences (at any level in the Enterprise Architecture. For example: (OT) Control and optimization of reactors, compressors, or other hazardous equipment (IT) Continuous Environmental Monitoring Systems (CEMS) that may result in fines and/or plant shutdown.
Special equipment and network design are required for hazardous areas (e.g., Industrial networks, firewalls, etc.).

## Slide 8
IT ROLES in PLANT ARCHITECTURES
IT skills may be the best alternative to manage projects in plant areas such as warehouses, administration areas, research laboratories, computer centers, etc.
These IT skills might include specialists in Database Design and Operation, Commercial Networks, Data Security, etc.
IT or Commercial Telecom experts may be requested by Control Engineers to participate in the design and configuration of traditional Ethernet or cellular networks that form part of Industrial networks (e.g. Process Data Historians or cellular steam trap monitoring). This is usually done through specifications written by IT and implemented by Control Systems.
Similarly, Control System Engineers may be requested to participate in the design of IT systems installed in hazardous industrial areas.
Notes: IT skills may be the best alternative to manage projects in plant areas such as warehouses, administration areas, research laboratories, computer centers, etc.
These IT skills might include specialists in Database Design and Operation, Commercial Networks, Data Security, etc.
IT or Commercial Telecom experts may be requested by Control Engineers to participate in the design and configuration of traditional Ethernet or cellular networks that form part of Industrial networks (e.g. Process Data Historians or cellular steam trap monitoring). This is usually done through specifications written by IT and implemented by Control Systems.
Similarly, Control System Engineers may be requested to participate in the design of IT systems installed in hazardous industrial areas.

## Slide 9
COMBINED IT AND CONTROL SYSTEM ROLES in PLANT ARCHITECTURES
Some large or particularly complex plant systems or applications may require ongoing participation of both Control Systems and IT experts. Even larger facilities may require both IT and Control Systems teams.
In these cases, Project Management or Plant Management will determine which discipline will lead the work. If two individuals or teams are responsible, then no one is responsible.
Industrial Telecom experts may be requested by Control Engineers to participate in the design and configuration of traditional Ethernet or cellular networks that form part of Industrial networks (e.g. Process Data Historians or cellular steam trap monitoring). This is usually done through specifications written by IT and implemented by Control Systems.
Similarly, Control System Engineers may be requested to participate in the design of IT systems installed in hazardous industrial areas.
Notes: Some large or particularly complex plant systems or applications may require ongoing participation of both Control Systems and IT experts. Even larger facilities may require both IT and Control Systems teams.
In these cases, Project Management or Plant Management will determine which discipline will lead the work. If two individuals or teams are responsible, then no one is responsible.
Industrial Telecom experts may be requested by Control Engineers to participate in the design and configuration of traditional Ethernet or cellular networks that form part of Industrial networks (e.g. Process Data Historians or cellular steam trap monitoring). This is usually done through specifications written by IT and implemented by Control Systems.
Similarly, Control System Engineers may be requested to participate in the design of IT systems installed in hazardous industrial areas.

## Slide 10
MAJOR ENTERPRISE SYSTEMS OPERATE AT MULTIPLE LEVELS
Most major Enterprise Systems operate at several levels in the architecture, for example:
  Production Management
  Maintenance Management
  Quality Control
  Engineering, Research and Development and other Major Enterprise Systems.
These systems typically comprise a large number of application programs designed for use by different Professional Roles to accomplish work processes and deliverables, as described below.
Notes: Most major Enterprise Systems operate at several levels in the architecture, for example:
Production Management
Maintenance Management
Quality Control
Engineering
Research and Development
These systems typically comprise a large number of application programs designed for use by different Professional Roles to accomplish work processes and deliverables, as described below.

## Slide 11
PRODUCTION MANAGEMENT SYSTEM LEVELS
ORDER PROCESSING & INVOICING
PRODUCTION PLANNING
PRODUCTION REPORTING
PRODUCTION SCHEDULING
PRODUCTION DATA CAPTURE
SCHEDULE CHANGES
OPERATOR INTERFACE
CONTROL AND INTERLOCKING
INVENTORY CONTROL
INVENTORY STATUS
SECS
MINS
HRS
DAYS
WEEKS
MNTHS
Time Base
Level
1
2
3
4
5
Control & Interlocks
Operator
Interface
Suprv.
Systems
Local Business
Prod'n Mgmnt
Applications
Production Management Systems span at least 5 levels in the architecture where they are used by different groups.
Function
Notes: Production Management Systems span at least 5 levels in the architecture where they are used by different groups.

## Slide 12
MAINTENANCE MANAGEMENT SYSTEM LEVELS
SECS
MINS
HRS
DAYS
WEEKS
MONTHS
Time Base
Control & Interlocks
Operator
Interface
Suprv.
MAINTENANCE COSTING
TECHNICAL SPECIFICATIONS
EQUIPMENT HISTORY
MAINTENANCE SCHEDULING
WORK ORDER CONTROL
EQUIPMENT MONITORING (LONG TERM)
EQUIPMENT MONITORING (REAL-TIME)
EQUIPMENT ALARMS
EQUIPMENT PROTECTION
PROFILE ANALYSIS
EXPERT SYSTEM EQUIP. ADVISORS
DOWNTIME REASON LOGGING
DEVICE FAILURE MONITORING
Systems
Local Business
Prod'n Mgmnt
Applications
Maintenance Applications may span 5 Levels in the Architecture, from Equipment Protection at Level 1, where the 4Rs range from milliseconds to hours, to Maintenance Costing, with 4Rs of days to months.
Level
Function
1
2
3
4
5
Notes: Maintenance Applications may span 5 Levels in the Architecture, from Equipment Protection at Level 1, where 4Rs range from milliseconds to hours,to Maintenance Costing with 4Rs of days to months.
Some designers prefer to separate Maintenance Applications on a separate industrial network (below the plant firewall. However, so many plant readings are shared with Production Management and even Quality Control that this creates more problems than benefits.

## Slide 13
SUPPLIER RATING
COST OF QUALITY
LAB INPUT
DATA CAPTURE
PREDICTIVE ALARMS
FINISHED GOODS RELEASE
RECIEVING INSPECTION
STATISTICAL QUALITY CONTROL
OPERATOR INPUT
STATISTICAL PROCESS CONTROL
PROCESS CONTROL (QUALITY LOOPS)
QUALITY ALARMS
COMPLAINT ANALYSIS
QUALITY APPLICATIONS LEVELS
SECS
MINS
HRS
DAYS
WEEKS
MNTHS
Time Base
Prod'n Mgmnt
Applications
Control & Interlocks
Operator
Interface
Suprv.
Systems
Local Business
SPECIFICATIONS
PROCESS CAPAB.
WHAT IF STUDIES
CALIBRATION
PROBLEM ANAL.
Quality applications also span several levels, from online analyzers at Level 1 to Complaint Analysis at Level 5 or 6. The nature of quality analyzers and measurements means that 4Rs at the control level may start at seconds rather than milliseconds.
Level
Function
1
2
3
4
5
Notes: Quality applications also span several levels, from online analyzers at Level 1 to Complaint Analysis at Level 5 or 6.
The nature of quality analyzers and measurements means that 4Rs at the control level may start at seconds rather than milliseconds.

## Slide 14
Logical and Physical Architectures provide a “framework” for the full set of Enterprise Systems.
Data highways and networks are shown as “horizontal” lines (since they connect devices at the same architectural level).
Data Flows that move up a level, immediately assume the 4Rs (Response, Resolution, Reliability and Resilience) of the higher level, even if the data flows back down.
Access between Levels (e.g., between Industrial and Office networks) should be controlled with Firewalls and/or Gateways.
Multi-level inter-application standards and protocols are required if applications are to communicate (e.g. OPC UA, ISA95, etc.).
Logical and Physical Architecture Diagrams are developed at increasing detail as a facility is designed and operated, and these provide a tool to communicate to the rest of the Enterprise.
KEY MESSAGES
Notes: Logical and Physical Architectures provide a “framework” for the full set of Enterprise Systems.
Data highways and networks are shown as “horizontal” lines (since they connect devices at the same architectural level).
Data Flows that move up a level, immediately assume the 4Rs (Response, Resolution, Reliability and Resilience) of the higher level, even if the data flows back down.
Access between Levels (e.g., between Industrial and Office networks) should be controlled with Firewalls and/or Gateways.
Multi-level inter-application standards and protocols are required if applications are to communicate (e.g. OPC UA, ISA95, etc.).
Logical and Physical Architecture Diagrams are developed at increasing detail as a facility is designed and operated, and these provide a tool to communicate to the rest of the Enterprise.

## Slide 15
AUTHOR
Gary has more than 40 years of experience with enterprise integration and optimization projects, including PERA master planning and project management.
As one of the initial authors of the PERA Handbook of Master Planning, he has used PERA Enterprise Architecture and Master Planning methodologies throughout his career including control and information systems for oil production, pipelines, refining and marine loading, petrochemicals, coal, gas, and oil-fired power plants, polyethylene, ammonia, explosives, paint, pulp and paper, food and beverage, and pharmaceuticals. LNG facilities included world-scale arctic, European, and US Gulf coast complexes.
infrastructure facilities included Fire, Police, and Emergency Response systems for major US cities, as well as emissions reporting and trading systems for more than 100 US Power Plants,