## Slide 1: What is Zero Trust in Plant IT Systems
PLC / RTU
Sensors
SCADA Servers
HMI
IIoT
DCS
ICS
MLM-018-D
Industry – Process
Principal Role – All
Professional Role – All
Enterprise Phase – All
Turn on your audio and click start to begin video
Notes: This MLM addresses the concept of Zero Trust in Plant IT systems from the point of view of an IT specialist.
Click the START button to advance.

## Slide 2: What is “Zero Trust”
Definition (recap from MLM-018-A):
  Zero Trust = “Never Trust — Always Verify.”
  Every connection request must be authenticated and authorized, regardless of source or network location.
Core Principles (IT standard):
  Verify explicitly (user, device, application).
  Use least privilege access.
  Assume breach — monitor continuously
    (This is a major difference with ACS systems)
Zero Trust is about removing implicit trust from systems and people.
  A Process Operator must log in to an H/R or maintenance system, even from a control room
Notes: What is Zero Trust?
Definition (recap from MLM-018-A):
  Zero Trust = “Never Trust — Always Verify.”
  Every connection request must be authenticated and authorized, regardless of source or network location.
Core Principles (IT standard):
  Verify explicitly (user, device, application).
  Use least privilege access.
  Assume a breach will occur — monitor continuously
    (This is a major difference with ACS systems)
Zero Trust is about removing implicit trust from systems and people.
For example, in Plant IT, we don’t give blanket access. A finance employee must log in every time they access payroll data — even inside HQ.
In a plant, the same mindset is retained: an operator must authenticate before accessing the HR or maintenance scheduling system, even from a control-room terminal.

## Slide 3: Why IT Zero Trust is Adopted
Zero Trust addresses the following problems:
  Networks are porous (cloud, remote work, third-party access).
  Credentials and endpoints can’t be assumed safe.
  Insider threats exist even inside “secure” networks.
Plant Example:
  ERP user connecting from home to approve maintenance purchase orders. Zero Trust ensures they log in via MFA, device is verified, and session monitored.
  The MES system gets accessed by a team member from the Quality team to release a batch, as the team member needs to access the MES system from the corporate network, and needs to be identified, we apply a Zero Trust approach.
Notes: Why is Zero Trust Adopted in IT systems?
Zero Trust addresses the following problems:
Networks are porous (having cloud, remote work, and third-party access),
Credentials and endpoints can’t be assumed safe,
Insider threats exist even inside “secure” network.
Plant Example:
ERP user connecting from home to approve maintenance purchase orders. Zero Trust ensures they log in via MFA, device is verified, and session monitored.
The MES system gets accessed by a team member from the Quality team to release a batch, as the team member needs to access the MES system from the corporate network, and needs to be identified, we apply a Zero Trust approach.

## Slide 4: How Zero Trust is Typically Implemented
Typical IT Implementation Layers:
  User: Central directory (Active Directory, Azure AD, IAM).
  Device: Endpoint verification, patch compliance, certificates.
  Network: Micro-segmentation, software-defined perimeter, firewalls.
  Applications: Access policies, API tokens, least privilege roles.
  Monitoring: SIEM, user behavior analytics, continuous validation.
Zero Trust is not one product — it’s an architecture of continuous validation.
Notes: How Zero Trust is Typically Implemented:
Typical IT Implementation Layers:
User: Central directory (Active Directory, Azure AD, IAM).
Device: Endpoint verification, patch compliance, certificates.
Network: Micro-segmentation, software-defined perimeter, firewalls.
Applications: Access policies, API tokens, least privilege roles.
Monitoring: SIEM, user behavior analytics, continuous validation.
Zero Trust is not one product - it’s an architecture of continuous validation

## Slide 5: Translating Zero Trust into an Industrial Context
Zero Trust is hard to transfer to ACS systems
  Latency: Authentication can’t delay real-time control loops.
  Safety: In many cases – such as in a manned control room – the DCS/SCADA screens (eg the ones containing the alarm lists) must always be visible and accessible
  Availability: “Deny by default” must not halt production.
  Legacy Systems: Many devices can’t perform modern authentication.
These challenges are often resolved by use of:
  Different devices and networks for IT and ACS systems
  Different standards for design and operation of systems
Notes: Zero Trust is hard to transfer to ACS systems because of challenges such as:
Latency: Authentication can’t delay real-time control loops.
Safety: In many cases – such as in a manned control room – the DCS/SCADA screens (eg the ones containing the alarm lists) must always be visible and accessible
Availability: “Deny by default” must not halt production.
Legacy Systems: Many devices can’t perform modern authentication.
These challenges are often resolved by use of:
Different devices and networks for IT and ACS systems
Different standards for design and operation of systems

## Slide 6: Further Information
Related MLMs
  MLM-018-A: Full and Zero Trust Models in Plants
  MLM-034-A – Understanding IT-ACS Integration
Additional Reference Materials
  Listing of all MLMs including video, PDF documents, PowerPoint, and SCORM downloads.
  Listing of PERA documents including original manuals, recent learning and reference materials.
  https://www.dragos.com/blog/implementing-zero-trust-in-operational-technology-ot-environments
  Please click here to provide feedback on this MLM.
Notes: Readers are invited to provide comments on how this content can be improved.
The Comment is routed to the author and subject matter experts for attention in revising the content and is an essential input to our quality control.

## Slide 7
Author – David Ariens
https://creativecommons.org/licenses/by-sa/4.0/
A mathematical engineer by training (class of 2010), David began his career at BASF as a data scientist and soon took on the role of European lead for industrial cybersecurity. In Antwerp he launched the site’s first Industry 4.0 projects, later heading the company-wide program across Europe. By the end of his tenure, he oversaw all industrial-digitization teams at BASF’s Antwerp complex.
In 2022 David became the Manager of Analytics for Industry, an Industrial DataOps specialist. A year later he teamed up with Willem van Lammeren to found The IT/OT Insider, now followed by more than 10 000 readers and listeners each month. In 2025 the duo expanded their mission with the ITOT.Academy, aiming to set the global standard for IT/OT learning.